Project Progress Report

3. Related Papers and Readings

There are many approaches that exist to detect vehicles and their relative position from your vehicle. Some of them are discussed below.
One of the approaches is based on a stereo vision system. The input is the data from the vision system and from a positioning-based system having a differential global positioning system (DGPS) and an inertial measurement unit (IMU).
The most common approach to vehicle detection is to use active acoustic-based sensors. Optical sensors are also used mainly because they are cheap and because there are potential new applications such as lane detection, pedestrian detection, traffic sign recognition, etc. Initially, regions of interest (ROIs) are computed and then lane markings are detected, thus reducing the vehicle search area. If no lane markings are detected, a basic ROI corresponding to a straight road is used instead. Possible vehicle regions are selected using a combination of symmetries (vertical edges, horizontal edges, and gray level symmetries) and white hat and Canny features together with a non-maximum suppression procedure which removes overlapped candidates. Also, a second camera was added to obtain a more detailed description of the leading vehicle’s features. Stereo processing results in a dense disparity map which allows the 3D position, the time-to-Collision, the width, and the length of the vehicle to be estimated accurately. The camera pitch angle is estimated dynamically by means of the so-called virtual disparity map from which regions corresponding to the ground-plane can easily be removed.
The project can basically be divided into two main parts. Firstly, detecting vehicles in the relevant ROI and secondly, calculating the distance of the detected vehicle in the given frame.
Calculating the distance can be done in various ways. We can use the concept of ‘Triangular Similarity’ or ‘Stereo Vision’ or ‘Optical flow’ in images. Stereo vision uses two cameras placed next to each other to get a 3D view (similar to how humans are able to view in 3 dimensions). Triangular Similarity uses the concept of using the value of the focal length of the camera, pixel width of the object in the image and the known distance of the object in reality and then using these values to calculate the distance of the object in images. Optical flow uses the concept of calculating the distance travelled by the same object in various frames of a given video. This can be helpful to deduce the fact that whether the object is approaching or not, towards the leading vehicle.

Some of the papers read and referred:
[1] Intelligent automatic overtaking system using vision for vehicle detection
[2] Object Detection and Measurement Using Stereo Images
[3] Object Distance Measurement using Stereo images.

4. Dataset: The dataset we are presently using (Stanford car dataset) has positive (images with cars) and negative (images without cars like background, road, tree, etc.) image sets.

Description of approach:

In order to solve the problem of vehicle detection, we made use of Support Vector Machine classifier to differentiate between positive and negative images based on the extracted features from each image. Our approach to the problem is as follows:

Firstly, we collected a set of both positive – images which contain cars, as well as negative – images which do not contain cars.
For each of the images in these sets, we extracted HOG (Histogram Of Gaussian) features and stored them in a .npy file along with the suitable class labels.
This file was then used to train our Linear SVM classifier.
For each of the test images, we implemented a sliding window mechanism which traversed through the full image, window-wise, extracting the features of each window, feeding it to the SVM classifier and obtaining the corresponding class labels. If features similar to that of a car were detected in the window, that window was marked as a hot-window. The area of the image with the highest number of hot-window-intersections is determined and a rectangular bounding box is made around the same – resulting in a rectangular region within the image which is supposed to have the highest probability of having a vehicle in it. Thus, resulting in detection of vehicle within the given test image.

Now comes the part where we need to find the distance of the vehicle in the given frame image. Here, we proceeded with the concept of Triangular Similarity.
Let’s say we have a vehicle (bounded box) with a known width W (average width of LMV- Light Motor Vehicles, is assumed). The vehicle is at some distance D from our camera. A picture of the vehicle behind is taken using our side-view camera and then we measure the apparent width in pixels P (the width of the bounding box). This allows us to derive the perceived focal length F of our camera:
F = (P x D) / W
As the overtaking vehicle continues to move closer or farther away from the camera, we can apply the triangle similarity to determine the distance of the vehicle to the camera:
D’ = (W x F) / P
We can plug the new apparent width (in pixels) in the above formula and determine the real distance of the overtaking vehicle from the leading vehicle.
Code Snippet:
# x1,y1,x2,y2 are the co-ordinates of the top-left and bottom right corners of the bounding box
def distance(x1, y1, x2, y2, F):
W = 1.0 # KNOWN_WIDTH (1.0 meter)
P = abs(x2 - x1)
D = ( F * W ) / P
return D

5. Future Work
We are planning to collect better data, that is, more specific to our problem statement. The dataset which will be more specific to overtake detection will be only frontal vehicle images. Also, these images should be from a side-view mirror’s angle. This can be achieved by taking a real time video of a road with some traffic from a camera kept at a stable position and angle.
Also, we have to figure out a better algorithm for car detection so that we can detect cars in real time. As of now, it takes a few seconds to detect a car in each frame of a video which needs to be reduced to at most 1 second.
We are also planning to use stereo vision technology to calculate the distance of the vehicle from the leading vehicle. It should give better results. For this we will have to fix two cameras on each side of the car at some distance from each other and use the left and right image to find the accurate distance of the overtaking vehicle.